## Slide 1: VCE IT Theory Slideshows by Mark Kelly 2016-2019 study design
By Mark Kelly, vceit.com, mark@vceit.com
Digital System Components
Version 1
Begin

## Slide 2: Contents
ITI U3O2 KK 14 - roles, functions and characteristics of digital system components used to
Input
Store
Communicate
Output
data and information.

## Slide 3: INPUT
Keyboards
  why is QWERTY universal?
  Dvorak
Mouses (mice? Discuss)
  Invented for the GUI OS
Touchscreens
  For portable devices – tablets, phones

## Slide 4: INPUT
Speech recognition
  Discuss: Why has it not taken over from primitive keyboards and mice, like in Star Trek?
Buttons, switches
  Custom hardware e.g. PC reset switches, MyKi machines, phone volume controls, “walk” buttons on traffic light poles.

## Slide 5: INPUT
Scanners
  Analogue to Digital conversion
  OCR (Optical Character Recognition) – printed text to electronic text – for example Google Books, Trove at the National Library.

## Slide 6: INPUT
Most archives, such as Trove at the National Library of Australia uses OCR to digitise printed newspapers.

## Slide 7: INPUT
Input device assessment criteria
  Speed
  Accuracy
  (Others?)

## Slide 8: STORE
Hard disk drives (HDD)
  Is mechanical, has moving parts
    aluminium platters spinning at 5,400 or 7,200 RPM
    read/write heads hover over the disk platters
  Any moving parts will eventually fail
  Great capacity (e.g. 8 terabtyes - TB)
  Good speed
  Low cost per TB
  Generate noise, heat.
  Consume reasonable amounts of electricity.

## Slide 9: STORE
Solid State disks (SSD)
  Electronic (like USB drive), no moving parts
    But memory cells will also fail after a given number of read/write operations.
  Silent (good for home theatre systems)
  Generates less heat than HDD
  Low power consumption.
  Poor capacity (e.g. 1 terabyte in 2016)
  Great speed (access times are much faster than HDD)
  High cost per TB compared to HDD (but reducing over time)

## Slide 10: STORE
Magnetic tape
  Going out of favour
  Tapes stretch, degrade over time
  May still be used by commercial sector
  Relatively slow read/write times
  Tapes need to be loaded/unloaded manually
  Good data capacity
  Media are easily portable

## Slide 11: STORE
Optical media – CD – DVD – BluRay
  CD capacity about 740MB
  DVD capacity about 4.7GB
  BluRay capacity about 25GB
Slow read/write speeds
Easily scratched and become unreadable
Dubious long-term storage lifetimes
Relatively little physical storage space needed

## Slide 12: STORE
Magnetic tape
  Going out of favour
  Tapes stretch, degrade over time
  May still be used by commercial sector
  Relatively slow read/write times
  Tapes need to be loaded/unloaded manually
  Good data capacity
  Media are easily portable
  Can be damaged/erased by strong magnetic fields

## Slide 13: STORE
Magnetic tape
  Going out of favour
  Tapes stretch, degrade over time
  May still be used by commercial sector
  Relatively slow read/write times
  Tapes need to be loaded/unloaded manually
  Good data capacity
  Media are easily portable

## Slide 14: STORE
Network Attached Storage (NAS)
  A group of HDD or SSD working as a team in a box
  Usually support RAID (Redundant Array of Independent Disks) to provide*
    data redundancy (one or more disks can fail without data loss) to improve reliability
    Speed (multiple disks can serve different data segments from a file at the same time)
    Backups via disk mirroring
  Centralised storage for offices – aids data sharing
*Depending on the type of RAID selected

## Slide 15
R.A.I.D.
Redundant Array of Independent Disks) arrays for reliability and/or speed.
RAID uses a group of hard disks that work as a single disk under a RAID controller.
Flavours of RAID: RAID0 to RAID10 (RAID 1 + RAID 0) offer reliability and/or speed (at ever-increasing cost). Includes mirroring (for reliability) and striping (spanning a logical single volume over several physical disks for greater performance – several simultaneous disk reads/writes are possible).
RAID disks are usually "Hot Swap“ – no server downtime to replace sick disks.
EXPENSIVE – needs justifying for small org
3-disk RAID array

## Slide 16: STORE
FLASH/NAND storage
  Includes familiar USB drives, SD drives
  Very portable
  Relatively low capacity in 2016 (e.g. 128GB)
  Relatively low read/write speeds using USB3
  Limited number of read/write cycles (like SSD)
  Can fail without warning
  Not affected by electromagnetic forces

## Slide 17: STORE
Floppy disks
  Hehehe. Yeah, let’s not even go there.

## Slide 18: COMMUNICATE
Mainly concerns networking hardware in a LAN (Local Area Network)

## Slide 19
Network Hardware
The main bits:
Modem
Cables
Network interface card (NIC)
Server (e.g. file server)
Switch
Router – often combined with ADSL modem, WAP, switch, print server, coffee maker etc)

## Slide 20
The modem Modulator/demodulator
Modulate (when uploading) = turn digital data into analogue sound for transmission over phone network.
Demodulate (when downloading) = convert sound back to digital data.

## Slide 21
Note!
Transmission speed is measured in bits per second (not Bytes per second!)
56Kbps modem downloads at a theoretical maximum of approx 56,000 bits per second (about 7KB/sec). Can only transmit (upload) at 33.6kbps.

## Slide 22
Hardware - NIC
The Network interface card (NIC) allows a stand-alone computer to connect to a network.
Can be cabled or wireless
Usually built into motherboards. Separate card not needed in most cases.

## Slide 23: Internet Choices Not all options are available to everyone, especially those not in major cities
ADSL, ADSL2, ADSL2+
(256Kbps-24Mbps speed caps)
Cable
(10-200Mbps)
Satellite
1 or 2 way (averaging 10-20 Kbps)
Dialup (analogue, av. 40Kbps)
WAN Wireless
3G/4G – internet access via mobile phone towers

## Slide 24
Hardware - NIC
Network Interface Card
Rated by speed: 10, 100, or ‘Gigabit’ 1000Mbps.
For a NIC to work at its maximum speed, all the other network devices between it and the server must have at least the same bandwidth (data-carrying capacity).
‘Auto-sensing’ e.g. 10/100/1000 NICs adjust themselves to the best possible speed.
Tip: go for GIGABIT NIC in servers

## Slide 25
Hardware – Switches and Hubs
Switches (and hubs) are connection points where cables can join up or be split.
Typically, a single incoming cable is split into multiple outgoing cables.

## Slide 26
Network segments
A network segment is a self-contained section of a network bounded by a bridge, router, or switch.
Using segments reduces network congestion.
Like classrooms in a school.

## Slide 27
Hardware – Routers
4 main roles…
Route packets across networks and internet
Act as a security device to guard the connection between a LAN and the outside world (another LAN or a WAN.)
Divide LANs into self-contained, protected areas, e.g. admin / student networks in a school.
Join dissimilar networks together, like a gateway (as the original routers used to be called)

## Slide 28
Hardware – Routers
Act as a firewall at home, complementing software firewalls like Windows Firewall
Can be programmed to only allow authorised incoming and outgoing traffic. E.g. can block certain sites, forbid MP3 music files to enter.
Most home routers also have a built-in mini-switch but remember … a switch is not a router!
Home routers often combine: switch, ADSL modem, print server, WAP

## Slide 29
Connections – UTP
UTP (Unshielded Twisted Pair) e.g. CAT6 (‘Category 6’)

## Slide 30
Connections – Fibre optic
Made of glass (or plastic)
Optical, not electrical – little signal fade
Optical Signals created by LED or laser
Multiple signals on a single fibre
Resists EMI (electromagnetic interference)
Light signals bounce down Fibre Optic cable using Total Internal Reflection.

## Slide 31
Connections – Fibre Optic
Core is as thin as a human hair
Not very flexible – needs thick protective coat
VERY fast
VERY high bandwidth
Very secure (can’t be tapped or snooped)
VERY long distance (>2km without repeaters)
Light weight, small size
Expensive adaptors to convert digital <> electrical signals

## Slide 32
Connections – Cables and wireless
Many fibre optic cable (‘FOC’) threads can be bound into a slim, single cable without their signals interfering with each other, giving massive data throughput.
FOC is replacing old, heavy, expensive copper cables to cross oceans
Warning! Sharks can damage your network!
Sharks get over-excited by the electromagnetic fields radiated by copper cable. FO is silent.

## Slide 33
Connections – Wireless
Data sent as radio signals between NICs and base stations (WAP=wireless access point)
short distances (e.g. 80m-200m), reduced by obstacles
Speeds of 54Mbps and increasing
Encrypted to prevent eavesdropping

## Slide 34: Wireless
Many PCs can connect to a base station, share its bandwidth
PCs can “roam” and will automatically connect to the base station that has the strongest signal
Wireless NICs and antennae now built into laptops

## Slide 35
Connections – Wireless
Good for temporary networks, or when PCs rarely needed in a location
Good for laptop-intensive places (e.g. classrooms, staffrooms). Great at home
Relatively expensive compared to cable, but a useful network add-on
Security concerns – never run it unsecured!
Wireless base station &
white radio antenna

## Slide 36
Server farms
On smaller networks, network services are performed by software in a single server.
On busy LANs, multiple servers share the work…
Login servers – authenticate users
Proxy servers – cache downloads
DHCP servers – allocate IP addresses
Print servers –manage print job queues
Web/FTP servers – serve web pages or files
Email servers –handle email

## Slide 37: OUTPUT
Monitors – CRT (extinct), LCD, plasma, data projectors
Printers – laser, ink jet, thermal
Audio – for warnings, information, voice cues
Custom controls – aeroplane altimiters, router LEDs, on/off signals on machines etc

## Slide 38: VCE IT THEORY SLIDESHOWS 2016-2019 study design
Mark Kelly
mark@vceit.com
vceit.com
These slideshows may be freely used, modified or distributed by teachers and students anywhere
but
they may NOT be sold.
they must NOT be redistributed if you modify them.
This is not a VCAA publication and does not speak for VCAA.
Portions (e.g. exam questions, study design extracts, glossary terms) may be copyright Victorian Curriculum and Assessment Authority and are used with permission for educational purposes. Thanks, guys!

## Slide 39: THANKS!
Because you’ve been so good, here’s a hardware picture you can look at while your teacher works out what to do next